## Slide 1: Reliability

## Slide 2: Reliability
Reliability is the probability that a failure may not occur in a given time interval.
Reliability of a unit or product is the probability that the unit performs its intended function adequately for a given period of time under stated operating conditions or environment.

## Slide 3
The reliability definition stresses four elements namely:
Probability
Intended function
Time
Operating conditions

## Slide 4
If T is the time till the failure of the unit occurs, then the probability that it will not fail in a given environment before time t is
R(t) = P(T>t).
Thus reliability is always a function of time. Since it is a probability, its numerical value is always between 1 & 0, i.e.
R(0) =1, R(∞) =0.

## Slide 5: Reliability engineering
Reliability engineering is an engineering field, that deals with the study of reliability.
Many types of engineering fields employ reliability engineers which use the tools and methodology of reliability engineering. For example:
  System engineers
  Mechanical engineers
  Automotive engineers
  Electronic engineers

## Slide 6: Reliability engineering
Reliability engineers rely heavily on :-
  Statistics
  Probability theory
  Reliability theory.
Many engineering techniques are used in Reliability Engineering:-
  Reliability Prediction
  Thermal Management
  Reliability Testing
  Accelerated Life Testing.
Reliability Program Plan

## Slide 7: Reliability engineering
Functions:-
  Develop the reliability requirements for the product
  Establish an adequate reliability program
  Perform appropriate analyses and tasks to ensure the product will meet its requirements.

## Slide 8: Quality
Quality of a device is the degree of conformance to applicable specifications and workmanship standards.
It is not concerned with the elements of time and environment.
An equipment which has undergone all quality tests may not necessarily be more reliable.

## Slide 9
The intended function of the device is related to the quality.
If an electric generator is expected to provide an output of 5 kW at 220 V under certain conditions, then 5 kW output at 220 V is the intended function of the generator.
Any deviation in either of these output parameters will be termed as the failure of the generator.

## Slide 10: Reliability And Quality
Reliability is the ability of the unit to maintain its quality under specified condition for a specified time
Quality is the ability of the unit to maintain its properties under specified condition for a specified time
Reliability is concerned with the performance of a product over its entire lifetime
Quality control is concerned with the performance of a product at one point in time, usually during the manufacturing process.

## Slide 11
Quality is associated with the manufacture whereas reliability is primarily associated with the design.
One can build a reliable complex system using less reliable elements but it is impossible to construct a “good” quality system from ”poor” quality elements.

## Slide 12: Failure
A failure is the partial or total loss or change in those properties of a device in such a way that its functioning is seriously impeded or completely stopped.
Some components have well defined failures: others do not.
The concept of failures and their details help in the evaluation of the quantitative reliability of the device.

## Slide 13: Failure Modes
Failures can be grouped into different modes depending upon the nature of failure.
Early failures
Catastrophic failures
Wear-out failure

## Slide 14: Bath-tub curve
A typical curve depicting the above three modes of failure is called as the bath-tub curve (due to its shape).
The bathtub curve is widely used in reliability engineering.
It describes a particular form of the hazard function which comprises three parts:
The first part is a decreasing failure rate, known as early failures.
The second part is a constant failure rate, known as random failures.
The third part is an increasing failure rate, known as wear-out failures.

## Slide 15: Bath-tub curve

## Slide 16
Infant
Mortality
failures
catastrophic failure rate
Wear-out
failures
Failure Rate
Time
Bath-tub curve

## Slide 17: Causes of failures
Poor design(component or system)
Wrong manufacturing techniques
Lack of total knowledge and experience
Complexity of equipment
Poor maintenance policies
Organizational rigidity and complexity
Human errors.

## Slide 18: Maintainability
It is a performance indice associated with equipments on which maintenance operation is performed.
It is the probability that a failed equipment is restored to operable conditions in a specified time (called down-time) when the maintenance is performed under stated conditions.

## Slide 19
It is also defined as the probability that failed equipment will be repaired within time t.
It is a function of repair time.
It is concerned with how long the equipment is down.

## Slide 20: Availability
It is the probability of time during which the equipment is available for use.
It is also defined as the probability that equipment is operating at time t.
It indicates the status of equipment at time t.
It is a performance index of maintained equipments.

## Slide 21
It is always associated with the concept of maintainability and integrates both reliability and maintainability parameters and depends on number of failures that occurs and how quickly faults are rectified.
It is expressed as:
Availability =
Uptime---the actual period for which the equipment is available for use.

## Slide 22: MTTF
Mean Time To Failure
It is a mean time until a design's or component's first failure, or disruption in the operation of the product, process, procedure, or design

## Slide 23: MTBF
Mean Time Between Failures
It is the predicted elapsed time between inherent failures of a system during operation.
The definition of MTBF depends on the definition of what is considered a system failure.

## Slide 24: MTTR
Mean Time To Repair, Restore, Respond Or Replace.
The average time taken to put a defective component or system back in working order.
The time taken to restore the system back to normalcy includes the period of diagnosis of the problem as well as its rectification.